## Slide 1: Project 1 ONOS and Mininet Installation
Environment Setup &
Basic Operation
Date : | 2019/03/05 (Fri.) 12:30
Deadline: | 2019/03/11 (Thu.) 23:59

## Slide 2: Overview
Mininet
ONOS
Virtual Machine
Use ONOS GUI to
see the topology
switch
host
host
switch
switch
switch

## Slide 3: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
  Start ONOS
    ONOS CLI
    ONOS Web GUI
  Activate basic ONOS APPs
    [Method 1] Via ONOS CLI
    [Method 2] Via ONOS GUI
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
    [Method 2] Custom Topology
Project Requirements
  Part 1: Answer Questions
  Part 2: Write a Custom Topology
  Bonus: Specify Hosts IP Address In Mininet

## Slide 4: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
Project Requirements

## Slide 5: Environment Setup
VirtualBox & ONOS & Mininet

## Slide 6: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
Project Requirements

## Slide 7: Virtualbox Installation
Oracle VM VirtualBox:
  a free and open-source hosted hypervisor for x86 virtualization,
  developed by Oracle Corporation.
Environment
  Ubuntu Desktop 16.04 (or 18.04) recommended
  Minimum Hardware settings
    2 Cores
    8GB RAM
    20GB HDD
For more installation detail, please refers to:
  SDN_Environment_Setup.pdf

## Slide 8: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
Project Requirements

## Slide 9: Bazel, ONOS, Mininet and OVS Installation
Bazel: free SW tool for “automation of building and testing of SW”.
  https://bazel.build/
Mininet: An instant virtual network on your computer
  http://mininet.org/
OVS (Open vSwitch): a multilayer software switch licensed under the open source Apache 2 license.
  https://www.openvswitch.org/
ONOS (Open Network Operating System): open source SDN controller The controller of SDN network
  https://www.opennetworking.org/onos/
Installation:
  Use TA-provided env_setup.sh

## Slide 10: Outline
Environment Setup
Basic Operation
  Start ONOS
    ONOS CLI
    ONOS Web GUI
  Activate basic ONOS APPs
    [Method 1] Via ONOS CLI
    [Method 2] Via ONOS GUI
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
    [Method 2] Custom Topology
Project Requirements

## Slide 11: Basic Operation
ONOS APPs & Custom Topo

## Slide 12: Outline
Environment Setup
Basic Operation
  Start ONOS
    ONOS CLI
    ONOS Web GUI
  Activate basic ONOS APPs
    [Method 1] Via ONOS CLI
    [Method 2] Via ONOS GUI
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
    [Method 2] Custom Topology
Project Requirements

## Slide 13: Start ONOS
Start ONOS server in localhost
The INFO “Updated node 127.0.0.1 state to READY” means that ONOS is successfully initiated
demo@SDN-NFV:~$ cd $ONOS_ROOT
demo@SDN-NFV:~/onos$ bazel run onos-local -- clean debug
# option 'clean' to delete all previous running status
# option 'debug' to enable remote debugging (port 5005)

## Slide 14: ONOS CLI
Bring up another new terminal and enter ONOS CLI
ONOS command “logout” to exit ONOS CLI
demo@SDN-NFV:~$ cd $ONOS_ROOT
demo@SDN-NFV:~/onos$ tools/test/bin/onos localhost
demo@root > logout

## Slide 15: ONOS Web GUI
Open web browser (e.g. Firefox)
  visit http://localhost:8181/onos/ui
    User/ Password: onos/ rocks
ONOS GUI (Graphical User Interface) tutorial
  https://wiki.onosproject.org/display/ONOS/Basic+ONOS+Tutorial#BasicONOSTutorial-ONOSGraphicalUserInterface
Notes: 說明MININET會預設掛HOST+圖
截圖上方不需要

## Slide 16: Outline
Environment Setup
Basic Operation
  Start ONOS
    ONOS CLI
    ONOS Web GUI
  Activate basic ONOS APPs
    [Method 1] Via ONOS CLI
    [Method 2] Via ONOS GUI
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
    [Method 2] Custom Topology
Project Requirements

## Slide 17: Activate basic ONOS APPs (Via ONOS CLI)
[Method 1]
Note: Use the following command to get more usage information
onos> apps -a -s # Show activated apps only
onos> app activate <name>
onos> app --help # display command help message

## Slide 18: Activate basic ONOS APPs (Via ONOS GUI)
[Method 2]
Click
Choose “Applications”
Choose “Reactive Forwarding”
Click
Click “OK”
1
2
3
5
4

## Slide 19: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
  Start ONOS
  Activate basic ONOS APPs
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
      Create a topology in Mininet controlled by ONOS
      Make hosts appear in ONOS GUI
    [Method 2] Custom Topology
Project1 requirements

## Slide 20: Create a topology in Mininet controlled by ONOS
Run Mininet with “--topo” & “--controller” options
  In this built-in topology, each switch would have one host
  “--controller” option adds remote controller
Use command “exit” in Mininet CLI to exit Mininet CLI
Controller
(ONOS)
s1
s2
s3
h1
h2
h3
$ sudo mn --topo=linear,3 --controller=remote,127.0.0.1:6653
127.0.0.1:6653

## Slide 21: Create a topology in Mininet controlled by ONOS
Note: Be sure to clean up the environment of Mininet after every time you exit Mininet CLI
$ sudo mn -c #clean and exit

## Slide 22: Make hosts appear in ONOS GUI
First, use “pingall” in the Mininet CLI
Press “h” in ONOS GUI to see hosts
Host information
s1
s2
s3
h1
h2
h3
mininet> pingall # ping between all hosts
Notes: Us pingall to
Onos detect host only when host send packets

## Slide 23: Outline
Environment Setup
  VirtualBox Installation
  Bazel, ONOS, Mininet and OVS Installation
Basic Operation
  Activate basic ONOS APPs
  Create a topology controlled by ONOS
    [Method 1] Via Mininet CLI
    [Method 2] Custom Topology
      Create a custom topology in Mininet
      Illustration of topology dictionary
Project1 requirements

## Slide 24: Create a custom topology in Mininet
Specify topology in Python and run the Python script
$ sudo mn --custom=sample.py --topo=mytopo \
> --controller=remote,ip=127.0.0.1,port=6653
s1(switch)
h1(host)
h2(host)
Sample.py
Custom topology

## Slide 25: Illustration of topology dictionary
Need to define a dictionary in Python script (i.e. sample.py) of custom topology
  Key is the short name passed to the appropriate option
  Value may be subclasses, constructors or functions
Option | dict. Name | Key : Value
--topo | topos | <short name> : <Topo constructor>
$ sudo mn --custom=sample.py --topo=mytopo \
> --controller=remote,ip=127.0.0.1,port=6653

## Slide 26: Outline
Environment Setup
Basic Operation
Project Requirements
  Part 1: Answer Questions
  Part 2: Create a Custom Topology
  Bonus : Specify Hosts IP Address In Mininet

## Slide 27: Project Requirement
Answer Questions (40%)
Create a Custom Topology (60%)
Bonus. Specify Hosts IP Address In Mininet

## Slide 28: Part 1: Answer Questions
Activate ONOS APPs
  When activating “org.onosproject.openflow”, what are the APPs which also be activated?
  Which APP enables hosts to ping each other?
Hint: Please refer to the reference “Basic ONOS Tutorial”[1] attached at the end of slide
$ netstat -tnlp #show only listening TCP sockets
Observe listening port
  Openflow protocol defines the TCP port for connection between controller and switch. What is the number of this port?
  Regarding to the previous question, which APP enables that TCP port be listening?
Hint: Observation of network connection
    bring up a new terminal
    use the command “netstat” to print network connection

## Slide 29: Part 2: Create a Custom Topology
Edit a Python script to build the following topology:
Hand in the Python script you edit in this part
s1(switch)
h1(host)
h2(host)
s2(switch)
s3(switch)
s4(switch)
h3(host)
h4(host)

## Slide 30: Part 2: Naming Convention & Command
Name of Python script: project1_<studentID>.py
Name of topology class: Project1_Topo_<studentID>
Name of dictionary’s key: topo_<studentID>
Command to execute your script:
$ sudo mn --custom=project1_<studentID>.py \
> --topo=topo_<studentID> \
> --controller=remote,ip=127.0.0.1:6653

## Slide 31: Part 2: Example of Naming Convention
In this case, should use the following command:
$ sudo mn --custom=project1_0748787.py \
> --topo=topo_0748787 \
> --controller=remote,ip=127.0.0.1:6653

## Slide 32: Bonus: Manually Assign Hosts IP Address In Mininet (I)
By default, Mininet will automatically assign an ip address and a subnet mask to each interface of each host
  (i.e. 10.0.0.1/8, 10.0.0.2/8, 10.0.0.3/8)
Reuse the topology created in part 2

## Slide 33: Bonus: Manually Assign Hosts IP Address In Mininet (II)
Manually assign each host’s ip address in the following format:
  192.168.0.<host_number>
Note: host_number starts from 1
e.g.
Take screenshots of the result of the Mininet command “dump” and “pingall” in Mininet CLI
Hand in the Python script you edit in this part
Note: activate “org.onosproject.fwd” in ONOS before “pingall”
mininet> dump # dump all the node info
… (result) …
mininet> pingall # ping between all hosts
… (result) ...
Host | IP Address
h1 | 192.168.0.1
h2 | 192.168.0.2
... | ...

## Slide 34: About Submit
Report & Python script

## Slide 35: Submit to new e3
Files
  Two Python scripts:
    project1_<studentID>.py
    bonus_<studentID>.py
  A report: project1_<studentID>.pdf
    Part 1: Answers to four questions
    Part 2: Take screenshots (ONOS GUI and CLI) and explain what you’ve done
    Bonus: Take screenshots (ONOS GUI and CLI) and explain what you’ve done
    Also write down what you’ve learned or solved
Submit
  Zip Python scripts and the report into a zip file
    Named: project1_<studentID>.zip
  Wrong file name or format would not be scored

## Slide 36: Thank you
Q & A

## Slide 37: Reference
Basic ONOS Tutorial
  https://wiki.onosproject.org/display/ONOS/Basic+ONOS+Tutorial
Introduction to Mininet
  https://github.com/mininet/mininet/wiki/Introduction-to-Mininet
MIninet Python API
  http://mininet.org/api/annotated.html
Manpage for Linux command
  netstat
    http://manpages.ubuntu.com/manpages/trusty/man8/netstat.8.html
  mn
    http://manpages.ubuntu.com/manpages/bionic/man1/mn.1.html

## Slide 38: Appendix: Network Topology for Mininet Emulation
Mininet employs lightweight virtualization features in the Linux kernel, including process groups, CPU bandwidth isolation, and network namespaces
An emulated host in Mininet is a group of user-level processes moved into a network namespace